## Slide 1: VHDL Taster Project
Philip Abbey

## Slide 2: Simple Project – Retro Alarm Clock
Basics
  Given
    Clock
    Pulse Per Second (PPS)
    Limited number of panel buttons
  Tell 24 hour time
Extensions
  Tell 12/24 hour time
  One or more alarms
  Stop watch mode (with lap)
  Count down timer
  Insights into synthesis results
FPGA
PPS
100 MHz Clock
Panel Buttons
n
28
Bell
Notes: 7 segment display has no visual representation. It is possible to write a Wish/TCL GUI but is a deviation from the main aims.

## Slide 3: Minimum Target
Drive 4 digits of a clock display
  These can simply be VHDL outputs driving four seven segment displays
  Use a design with a single clock for all synchronous logic
Provide a means of setting the time via a small number of “buttons” (design inputs)
  Set / Up / Down (as required)
  Using a finite state machine or otherwise…
A test bench to demonstrate the design
Submit your design via Git for review
Keep a list of the topics you discover you don’t know for discussion

## Slide 4: Tools
As a minimum you will need a Xilinx Vivado Webpack installation
  Provides both simulation and synthesis
  No licence required
  \\lead\Xilinx\Vivado 2020.1\Xilinx_Unified_2020.1_0602_1208.tar.gz
An alternative is to install Quartus Prime Lite
  Provides synthesis and
  A free but limited version of ModelSim
    You might like to create a compilation script (batch file) using vlib, vmap, vcom (and vsim) to avoid repetitive point & click
  \\lead\IT Software Library\General Q-T\QuartusPrime\QuartusLiteSetup-20.1.1.720-windows.exe
Notes: Xilinx's Vivado (I think this is 'Webpack' too when no license is used)
\\lead\Xilinx\Vivado 2020.1\Xilinx_Unified_2020.1_0602_1208.tar.gz
Intel's Quartus Prime
\\lead\IT Software Library\General Q-T\QuartusPrime\QuartusLiteSetup-16.1.0.196-windows.exe
\\lead\IT Software Library\General Q-T\QuartusPrime\QuartusLiteSetup-20.1.1.720-windows.exe

## Slide 5: Stretch Opportunities
Functional
  Swap the clock’s settings between 12h and 24h display
  Set one or more alarms to be optionally triggered by an “alarm on” setting
  Stop watch mode (with lap)
  Count down timer
Synthesis
  Choose any device you fancy, it matters little here
  “Elaborate” your design to generic gates and understand the logic inferred by your code
  Inspect the log file to identify things that look ominous
    Search the Internet to find out what they mean (we’ve all made those mistakes)
  Be ready to talk through the key features of your code and how it is realised in logic gates
  “Synthesis” (mapping to a particular technology) and explain how generic gates are mapped to a real device
    You will get all sorts of warnings, lack of constraints, pin allocations etc. Ignore them.

## Slide 6: Stretch Opportunities
Swap Vivado’s simulator for ModelSim
  You are offered a rudimentary “display” to drive
  Your VHDL outputs can be hooked up to the display using TCL
  Instructions are provided at the end
We appreciate this tool may not be available for your use
You can get a free version of ModelSim by installing the Quartus Prime Webpack synthesis tool which includes a limited edition of ModelSim and is sufficient for this task. You are not obliged to do this.

## Slide 7: Not Expected
Writing constraints for synthesis
Understanding timing reports
Re-working your code to resolve timing issues from synthesis
Clock domain crossings
  Use a single clock for all synchronous logic

## Slide 8: Hints
VHDL is a hardware description language
  Think of the logic first then write the code to describe it
If you’re not enjoying this job as much as I do each day, you’re doing it wrong.
  Have some fun
VHDL Tutorials
  VHDL Whiz
  Nandland
  TutorialsPoint
  FPGA Tutorial
  FPGA4student
NB. Nandland have a known errata
  They are slightly confused about some details of finite state machines
  Look else where for that!

## Slide 9: Vivado Installation
This will occupy 780 MB on completion

## Slide 10: Vivado Installation 1
Check you PC’s disk space
  Ensure you have ~55GB spare for Vivado ver 2019
  ~110GB for ver 2022!
  Actually, a Webpack installation can be nearer to a mere 22GB or 85GB respectively.
Using the following options we can trim the installation down
  Vivado (not Vitis)

## Slide 11: Vivado Installation 2
Vivado ML Standard

## Slide 12: Vivado Installation 3
Trim the devices down if you are short on disk space
  E.g. just Kintex UltraScale
Keep DocNav
  In case Vivado offers you a help link
No need for Matlab Simulink
No need for cable drivers
You can return to the installer for anything you missed

## Slide 13: Simulated Display - Optional
ModelSim only (sorry)

## Slide 14: VHDL Assumptions or Pre-requisites
library ieee;
use ieee.std_logic_1164.all;
package sevseg_pkg is
<snip>
type time_disp_t is array (0 to 3) of std_logic_vector(6 downto 0);
<snip>
end package;
sevseg_pkg.vhd
entity time_display is
port(
<snip>
disp : out work.sevseg_pkg.time_disp_t;
<snip>
);
end entity;
time_display.vhd
A 4 element array of 7 bits each to drive the graphical display

## Slide 15: Driving the display from TCL
Save this TCL file locally
Amend your VHDL test bench simulation signal names to match:
  Delete any you do not plan on using and amend “proc display_cursor” to suit.
Open your simulation in ModelSim
Source the sevseg_display.tcl TCL script in the ModelSim TCL shell
  This should open up the graphical display in a separate window and set up the update trigger
  source {path\to\sevseg_display.tcl}
run -all multiple times until completion
  As provided, the update event calls a function which includes a “stop” call to pause the simulation so you can see the change to the display before it runs to the next value too quickly.
set disp {/test_time_display/disp}
set alarm {/test_time_display/alarm}
set am {/test_time_display/am}
set pm {/test_time_display/pm}

## Slide 16: Good Luck!